## Slide 1: NanoVNA-F & NanoVNA
NanoVNA-F 4.3”
~$120 - $150
NanoVNA 2.8”
~$35 - $65

## Slide 2: NanoVNA Overview
Low price precision measurement test equipment
Small portable PC connectable device
Requires calibration before using to ensure accuracy
Open source architecture – hardware and software
Uses include measuring:
  Inductance
  Complex antenna impedance
  Chokes
  Gain
  Attenuation
  Align filters
  Measuring coax length and finding location of defects in a feedline

## Slide 3: Navovna – General Description
  NanoVNA is a vector network analyzer (not computer network)
  Typical measurement range is 50Khz to 1.5Ghz (accuracy decreases with frequency)
  Distinguishing features (from other test devices e.g. scaler antenna analyzers):
    Measures amplitude and phase providing complex numbers
    Real and imaginary elements of electrical features
      Impedance as Z=R+jX instead of Z only (scalar antenna analyzers)
    2 high-frequency ports/connectors allowing measurement of amplitude and phase as well as forward and reflected power.
      Port 1 (CH0/TX) acts as the output of the incident signal as well as measurement port for the reflected signal
      Port 2 (CH1/RX) receives the signal of a Device Under Test such as a filter
      Scatter parameters/S-parameters – S11 and S21
        S11 = measured at port 1, incident from port 1 (reflection)
        S21 = measured at port 2, incident from port 1 (transmission)
Port 1
Port 2

## Slide 4: Hardware versions and construction
High quality models and many cheaper clones
  Sold with or without batteries, get one with the battery included
  Sold with or without shielded ports (different from shielded case)
  Cheaper models have inferior and fewer accessories, e.g. # of SMA connectors and coax leads (RG174 vs. RG316)
  NanoVNA 2.8” screen – original marketed by Hugen enclosed in a protective plastic (3D printed) case
  NanoVNA-F 4.3” – Deepelec sold through Aliexpress is a high quality offering with metal case and complete accessory package
  Required calibration accessories include: short, open, load, thru connectors (SMA)

## Slide 5: NanoVNA-F & NanoVNA
NanoVNA-F 4.3”
~$120 - $140
NanoVNA 2.8”
~$35 - $65
3D printed case often extra $13
High quality models include metal enclosure and RG316 cables

## Slide 6: Using the NanoVNA and understanding its output Three Chart Types: Linear, Smith and Polar
Linear – used to display LOGMAG, PHASE, DELAY, SWR, LINEAR, REAL, IMAG, RESISTANCE AND REACTANCE
  Always 9 horizontal lines on the plot of the hardware device

## Slide 7: Using the NanoVNA and understanding its output Three Chart Types: Linear, Smith and Polar
Smith and Polar used to simultaneously portray complex impedance over frequency sweep – Smith and Polar provide different view of same data

## Slide 8: Using the NanoVNA and understanding its output
Traces
Data is measured with traces - up to 4 (firmware dependent) represented with different colors (more when using PC interface and software)
Displayed as plots on the screen and as text on the left and top coded by color
Traces can be switched on and off and are associated with C11 or C21
Available formats of measurement data
  LOGMAG: magnitude of signal in decibel relative to the incident signal
  PHASE: phase of signal in degrees relative to the incident signal
  DELAY: group delay versus frequency, typically in picoseconds or nanoseconds
  SMITH: complex impedance at the selected port – real in ohms and imaginary in inductance or reactance, centered on 50 ohms
  SWR/return loss
  POLAR: complex reflection response
  LINEAR: norm of the complex reflection response transmission coefficient
  IMAG: imaginary part of the complex reflection response transmission coefficient
  RESISTANCE: real part of the impedance in ohms
  REACTANCE: imaginary part of the impedance in ohms

## Slide 9: Traces of 50ohm load on 4” RG316 cable at 50kHz

## Slide 10
Markers - Set by the user for specific frequency data points and indicated on the screen by colored triangles (NanoVNA Saver 4 plot – 3 marker display example)
Analytical results provided for each marker that is set (Homebrew moxon for 1.25M)
VSWR
Return Loss
Z - Impedance
Z - Impedance
Complex Impedance

## Slide 11: Traces and Markers as on Device

## Slide 12
- Menu Structure

## Slide 13: Calibration
“The NanoVNA is a very capable, high precision measurement device. But unlike some other instruments, it needs careful calibration before reliable measurement results can be expected. This is primarily due to the fact, that a VNA provides phase information, not only magnitudes. Bear in mind, that we are talking about a sensitivity of up to 70 dB. This is one in ten million!”
The phase of a signal is changed by many effects e.g.
  Distance, type of feedline, connector type – which become more critical as frequency increases into VHF+ range
Two types of calibration – Full S21 (thru) and Partial S11 (reflected)
  S11 – open, short, load
  S21 – open, short, load, isolation, thru
5 calibration memories C0-C4, can be set for various uses/frequency ranges

## Slide 14: Calibration reference plane
Is the location where the DUT will be connected to the NanoVNA
It is very important, that the SOLT calibrators are fitted at the position of the reference plane during the calibration process – and ideally to the termination connector type!
  Cable and connector effects are eliminated with proper reference plane calibration
Reference plane impacts become more significant as frequency increases (e.g. cable length)
Connector specific calibration standards

## Slide 15: PC Software – NanoVNA Saver
This is probably the most comprehensive software currently available for the NanoVNA. As this software is based on Python it can be installed on Windows, Mac, and Linux.
  Check it on GitHub, where you will find the latest release and instructions for installation.
  The following illustrations are based on the NanoVNA Saver 0.2.2 release running on a Windows 10 computer.
Note: Once the NanoVNA is connected to the PC, a software calibration is required for accurate measurement, like the firmware calibration for the standalone device
  1st the hardware unit should be calibrated
  2nd the software is calibrated
Other software products include: NanoVNA-Web-Client, NanoVNASharp, TAPR VNA, Matlab/Labview

## Slide 16: PC Software – NanoVNA Saver Cont. – Display Setup
Display settings
Allow up to 6 plots of 12 graph types
Allow additional markers
Sets line size and background
Display ham bands
Set VSWR limits

## Slide 17: NanoVNA Saver Cont. – Sweep Control & Markers
Seep Control
Set frequency limits
  Note - Always 101 measurements between limits
  Reducing sweep limits increases granularity
Set single, continuous or average sweep
Set number of sweeps
Set number of measurements to discard (outliers)
Set degree to “pad” band limits
Name sweep for future use

## Slide 18: Analysis examples: TDR estimate of cable length with 50 ohm load (CH0 S11 plot)
Cable length
56’ 3”
VSWR
Return Loss
Complex impedance
50 Ohms

## Slide 19: Analysis of a Disconne antenna – 30Mhz to 1Ghz (CH0 S11 plot)
Smith Cart – complex impedance
Return Loss
VSWR
Z - impedance

## Slide 20: Analysis of a Low Pass Filter (CH1 S21) – What Ham Band is this designed for?
Return Loss
VSWR

## Slide 21: Analysis of a 2nd Low Pass Filter (CH1 S21) – What Ham Band is this designed for?
Return Loss
VSWR

## Slide 22: What is the Device Under Test?
Return Loss
VSWR

## Slide 23: Analysis of a 6M Omni Angle
Return Loss
VSWR

## Slide 24: Analysis of a 6M 4 Element Yagi (with comparison to Omni Angle)
Return Loss
VSWR
Memo:
Omni Angle
Return Loss Curve

## Slide 25: Analysis of a 1.25M (222Mhz) 5 Element Yage
Return Loss
VSWR

## Slide 26: Analysis of a 2M/70cm Dual Band Yagi
Return Loss
VSWR