## Slide 1: Your First CW QSO What You Need To Know
Bob Karz, K2OID
December 18, 2018

## Slide 2: The Band Plan – Where are the CW Stations?
Hint – They’re RED

## Slide 3: The Band Plan – Where are the CW Stations?

## Slide 4: The Band Plan – Where are the CW Stations?
Look Towards the Top of the CW Sub-band
  Typically 50 to about 70 Khz above band edge
  Slowest CW
  Less QRM
Stay below the unofficial Data frequencies (RTTY, FT8, etc.)

## Slide 5: How to Initiate a Contact
CQ CQ CQ CQ DE W2XYZ W2XYZ K
  Number of repeats is up to the operator
Answer at calling station’s speed or slower
  Not Faster
  Send his/her call once “DE” your call twice then “K”
If you call the CQ, first send “QRZ DE K2OID” to be sure the frequency is clear
  I suggest CQ CQ CQ DE K2OID repeated twice then “K”
  Ideally you want only 1 answer

## Slide 6: The Initial Exchanges
The call:
  CQ CQ CQ DE W2XYZ K
My Answer:
  W2XYZ DE K2OID K2OID K
His/Her reply:
  K2OID DE W2XYZ – RR ES TNX FER THE CALL – UR RST IS 569 569 ES QTH IS NR BINGHAMTON, NY NR BINGHAMTON, NY - NAME IS GEORGE GEORGE – SO HW? AR K2OID DE W2XYZ K

## Slide 7: OK. I recognize some of this. What does it mean in English?

## Slide 8: The Initial Exchanges
The call:
  CQ CQ CQ DE W2XYZ K
My Answer:
  W2XYZ DE K2OID K2OID K
His/Her reply:
  K2OID DE W2XYZ – RR ES TNX FER THE CALL – UR RST IS 569 569 ES QTH IS NR BINGHAMTON, NY NR BINGHAMTON, NY - NAME IS GEORGE GEORGE – SO HW? AR K2OID DE W2XYZ K
Roger Roger and thanks for
your
Location
and
Signal Report
near
how copy
That’s it for
this go around
Anyone want a contact?
From
Back to you

## Slide 9: The Initial Exchanges
The call:
  CQ CQ CQ DE W2XYZ K
My Answer:
  W2XYZ DE K2OID K2OID K
His/Her reply:
  K2OID DE W2XYZ – RR ES TNX FER THE CALL – UR RST IS 569 569 ES QTH IS NR BINGHAMTON, NY NR BINGHAMTON, NY - NAME IS GEORGE GEORGE – SO HW? AR K2OID DE W2XYZ K
You repeat your call twice in your first call as insurance that the other station has your call correct.
Note that dashes are used in place of periods to separate “sections”

## Slide 10: The Initial Exchanges
The call:
  CQ CQ CQ DE W2XYZ K
My Answer:
  W2XYZ DE K2OID K2OID K
His/Her reply:
  K2OID DE W2XYZ – RR ES TNX FER THE CALL – UR RST IS 569 569 ES QTH IS NR BINGHAMTON, NY NR BINGHAMTON, NY - NAME IS GEORGE GEORGE – SO HW? AR K2OID DE W2XYZ K
He/She sends K2OID DE W2XYZ so that:
  You know he/she has your call correct
  That W2XYZ is actually in QSO with you, not someone else

## Slide 11: The Initial Exchanges
The call:
  CQ CQ CQ DE W2XYZ K
My Answer:
  W2XYZ DE K2OID K2OID K
His/Her reply:
  K2OID DE W2XYZ – RR ES TNX FER THE CALL – UR RST IS 569 569 ES QTH IS NR BINGHAMTON, NY NR BINGHAMTON, NY - NAME IS GEORGE GEORGE – SO HW? AR K2OID DE W2XYZ K
Before anything else you will hear your signal report sent twice because he/she has no idea how well you are copying his/her signal

## Slide 12: Interpreting the QSO so far
The Signal Report or RST
  Readability (Scale from 1 – 5)
    Most of the time it will be “5” (perfectly readable)
      4 means some difficulty (perhaps interference (QRM) or static/noise (QRN)
      3 (rare) means significant difficult
      2 (even more rare) means barely copyable
      1 means no copy
  Strength (Scale from 1 – 9)
    More or less follows your S-Meter reading
    I give 9 to very strong signals, 7 or 8 to strong signals, 5 or 6 to average signals, 3 or 4 to weak signals, and 1 or 2 to very weak signals

## Slide 13: Interpreting the QSO so far
  Strength (Scale from 1 – 9) Cont’d
    Be honest about strength, don’t just repeat what the other station sends
    In contests most stations just send “599” as in:
      UR 599 – PSE RPT ALL
    Besides QRN and QRM, a common “add” is QSB or signal fading e.g. 599QSB
      If there is QSB, I give a signal report based on the strongest it has been
  Tone (Scale from 1 – 9)
    This is a hold over from the spark and vacuum tube days. It should be 9 unless the other signal is truly bad (e.g. 60 Hz hum or chirp)

## Slide 14: The Initial Exchanges
The call:
  CQ CQ CQ DE W2XYZ K
My Answer:
  W2XYZ DE K2OID K2OID K
His/Her reply:
  K2OID DE W2XYZ – RR ES TNX FER THE CALL – UR RST IS 569 569 ES QTH IS NR BINGHAMTON, NY NR BINGHAMTON, NY - NAME IS GEORGE GEORGE – SO HW? AR K2OID DE W2XYZ K
QTH and Name
  After the RST, the QTH is sent first
    I generally send “NR ROCHESTER, NY” twice
    Your name is the final information on the first exchange (again sent twice)
    Note that many stations have computers with QRZ.com, so they have your information

## Slide 15: The Initial Exchanges
Your typical response
  W2XYZ DE K2OID – FB GEORGE – NICE TO MEET U – UR RST IS 579 579 ES QTH IS NR ROCHESTER, NY NR ROCHESTER, NY - NAME IS BOB BOB – RIG HR IS FLEX 6300 AT 100 W TO A DIPOLE AT 50 FT – WX IS CLDY WID SNOW - HW? AR W2XYZ DE K2OID K

## Slide 16: The Initial Exchanges
fine business
you
here
weather
watts
cloudy with
temperature
Your typical response
  W2XYZ DE K2OID – FB GEORGE – NICE TO MEET U – UR RST IS 579 579 ES QTH IS NR ROCHESTER, NY NR ROCHESTER, NY - NAME IS BOB BOB – RIG HR IS FLEX 6300 AT 100 W TO A DIPOLE AT 50 FT – WX IS CLDY WID SNOW – TEMP IS 28F - HW? AR W2XYZ DE K2OID K

## Slide 17: The Initial Exchanges
Your typical response
  W2XYZ DE K2OID – FB GEORGE – NICE TO MEET U – UR RST IS 579 579 ES QTH IS NR ROCHESTER, NY NR ROCHESTER, NY - NAME IS BOB BOB – RIG HR IS FLEX 6300 AT 100 W TO A DIPOLE AT 50 FT – WX IS CLDY WID SNOW - HW? AR W2XYZ DE K2OID K
His/Her typical reply
  His rig
  His weather
  Perhaps a question or comment for your response

## Slide 18: The Initial Exchanges
Some possible rag chew topics
    How long a ham
    Age
    Equipment
    Been to your QTH
Some QSOs are very short while others can last hours

## Slide 19: Hints and Tips
Always begin your transmission with feedback on copy For example:
  FB GEORGE – SOLID COPY
  QRM TT TIME BUT GOT MOST
  QTH AGN PSE BK
If the other station is sending too fast for you don’t hesitate to QRS For example:
  I AM NEW TO CW – PSE QRS
Abbreviations are optional!!!

## Slide 20: Hints and Tips
Never hesitate to have something you missed repeated.
Remember that you are in the low speed sub-band.
  It is expected that less experienced CW ops (“not show offs”) will be found there.
Dashes (-) are often used in place of other punctuation

## Slide 21: Hints and Tips
Signing “KN” rather than “K” means “no breakers”
  Used most often during rag chew with DX or a rare state
  Otherwise you are welcomed to “break in” between exchanges
    Useful when going after that “new one”

## Slide 22: Tying the Ribbon
When it’s involuntary (e.g. QRN, QRM, QSB)
  On your turn say some thing similar to: SRI – NO CPY CUZ QRM – 73 ES TNX QSO – HPE CU AGN – SK W2XYZ DE K2OID CL
When you have other commitments, say so:
  XYL CLG ME TO DINNER
  MUST CATCH SOME ZZ
More commonly:
  TT IS ALL FROM HR – QRU?

## Slide 23: Tying the Ribbon
When it’s involuntary (e.g. QRN, QRM, QSB)
  On your turn say some thing similar to: SRI – NO CPY CUZ QRM – 73 ES TNX QSO – HPE CU AGN – SK W2XYZ DE K2OID CL
When you have other commitments, say so:
  XYL CLG ME TO DINNER
  MUST CATCH SOME ZZ
More commonly:
  TT IS ALL FROM HR – QRU?
Sorry – no copy because of QRM
Thanks for the contact – Hope to see you again
This is my last transmission
(also “Silent Key” e.g. deceased)
Station is closing down (or clear for this QSO)
Wife calling
Sleep
That’s all from here – do you have anything more for me?

## Slide 24: Confirming a contact (QSL)
If you want a confirmation (or QSL) now is the time to ask for it. For example:
  PSE QSL or PSE QSL VIA BURO
  Answer will probably be QSL SURE
Note: QSL also means “I heard you”, more or less synonymous with RR. “QSL?” means “did you copy what I just sent?”

## Slide 25: Confirming a contact (QSL)
If you want a confirmation (or QSL) now is the time to ask for it. For example:
  PSE QSL or PSE QSL VIA BURO
  Answer will probably be QSL SURE
Note: QSL also means “I heard you”, more or less synonymous with RR. “QSL?” means “did you copy what I just sent?”
Please
ARRL QSL Bureau

## Slide 26: The Final Exchange
The final exchange for both sides ends with an “SK” then the call signs and finally “CL”. For example:
TNX NICE QSO – GE – SK AR W2XYZ DE K2OID CL

## Slide 27: The Final Exchange
The final exchange for both sides ends with an “SK” then the call signs and finally “CL”. For example:
TNX NICE QSO – GE – SK AR W2XYZ DE K2OID CL
Good evening

## Slide 28: …But wait! There’s More
Final flourishes
  After the “final” transmissions (the CLs) there is often a “CW goodbye handshake” without call signs
  Technically against the rules but everyone does it
  Example:
    GE BOB E E (two spaced dits)
    GE GEORGE E E

## Slide 29: Final Remarks
CW is really both a shorthand and a language
  For us English speakers it is relatively easy to master
    It has English syntax
    Most abbreviations are of English origin
Once you get on the air, you will quickly pick up the way things work
You’ll see why many of us think of it as the most elegant and enjoyable operating mode

## Slide 30: CW Abbreviations
Below are some CW abbreviations that I use
    73 Best Regards
    88 Love & Kisses
    A Number 1
    ABT About
    AGN Again
    ANT Antenna
    B4 Before
    BCNU Be Seeing You
    BK Back or Break
    BURO QSL Bureau
    CL Closing Station Down (or Clear in final transmission)
    CLDY Cloudy
    CLR Clear
    CONDX Conditions
    CONGRATS Congratulations

## Slide 31: Common CW Abbreviations
  CPY Copy
  CQ General Call for a QSO (Contact)
  CUZ Because
  DE From (eg... W3AA de W3DF)
  DSW See You Again (Russian)
  DWN Down
  DX Long Distance Contact, or a Rare Station
  EL Element (as in 3 EL Yagi)
  ES And
  FB Fine Business (Ham jargon for very good)
  FD Field Day
  FER For
  FIST Unique characteristic of an operator’s sending of CW
  FONE Phone (as in AM or SSB)
  FM From or Frequency Modulation
  FREQ Frequency
  GA Good Afternoon or Go Ahead

## Slide 32: Common CW Abbreviations
  GB Good Bye
  GD Good or Good Day GE Good Evening GG Going
  GL Good luck GM Good Morning GMT Greenwich Mean Time (standard time used by hams) GN Good Night GND Ground GP Ground Plane GUD Good HAM Amateur Radio Operator HI HI Laughter on CW HNY Happy New Year HPE Hope HR Here

## Slide 33: Common CW Abbreviations
  HV Have HW, HW? How, or How Do You Copy Me? II, II II II Error K Please Transmit KN Only the station I am working should transmit KNW Know LID Poor Operator Don’t confuse with “SOLID” LP Log Periodic (type of directional antenna) or Long Path LSB Lower Sideband LW Long Wire (type of antenna) MGR QSL Manager MNI, MANI Many MSG Message MULT Multiplier N No or the number 9. (599 IS 5NN IN MORSE) NIL Nothing Heard or No Copy

## Slide 34: Common CW Abbreviations
NW Now OM Old Man (Ham jargon for an experienced operator) OP Operator, or Name OPR Operator or Operate PSE Please PWR Power QRL The frequency is busy Is the frequency busy? QRM Your transmission is being interfered with. Is my transmission being interfered with? QRN I am troubled by static. Are you troubled by static? QRO Increase power. Should I increase power? QRP Decrease power. Also a station using low power Should I decrease power? QRQ Send faster. Should I send faster? QRS Send slower. Should I send slower? QRT Stop transmitting. Should I stop transmitting?

## Slide 35: Common CW Abbreviations
  QRU I don’t have anything more. Do you have anything more? QRV I am ready. Are you ready? QRX Please standby for ... Should I standby? QRZ You are being called by ... Who is calling me? QSB Your signal is fading Is my signal fading? QSK I can operate break-in Can you operate break-in? QSL I acknowledge receipt Do you acknowledge receipt? QSO I can communicate with ... Can you communicate with ...?
  QSY I will change my transmit frequency Should I change my transmit frequency?
  QTH My location is ... What is your location?
  R, RR Message Received or Correct, or Roger (affirmative)
  RCVR Receiver
  RIG Equipment
  RPRT or RPT Report or Repeat

## Slide 36: Common CW Abbreviations
  RX Receiver
  SHUD Should
  SIG Signal
  SK This is my last transmission
  SKED Schedule
  SP Short Path
  SRI Sorry
  STN Station
  SWL Short Wave Listner
  T Short hand for the number Zero
  TEMP Temperature
  TEST Contest
  TIL Until
  TKS Thanks
  TCVR Transceiver
  TT That
  TU Thank You

## Slide 37: Common CW Abbreviations
  TX Transmitter
  TNX Thanks
  U You
  UR Your
  USB Upper Sideband
  UTC Universal Time Coordinated (same as GMT)
  VERT Vertical Antenna
  VFO Variable Frequency Oscillator
  VY Very
  W Watts
  WID With
  WKD Worked (Ham jargon for making a contact with a station)
  WKG Working
  WPM Words Per Minute (a measure of code speed)
  WRK Work

## Slide 38: Common CW Abbreviations
  WUD Would
  WX Weather
  XCVR Transceiver
XMTR Transmitter
XTAL Crystal
XYL Wife
YL Young Lady
Z Zulu, GMT, or UTC Time (all the same)
ZZ Sleep